## Slide 1
SMART SPICE
DISPENSER
SYSTEM
Using 8051 Microcontroller & Arduino
Vansh Kukkar • Krish Kumar Kedia • Ronit Vishwakarma • Om Patil • Prashant Kumar Moharana
24BEC1368 | 24BEC1506 | 24BEC1347 | 24BEC1418 | 24BEC1500

## Slide 2
AIM & OBJECTIVE
🎯 AIM
Design and implement a Smart Spice Dispenser System using 8051 microcontroller and Arduino interfacing that can automatically dispense spices in controlled quantities using servo motors, and measure weight using a load cell with HX711 module — displaying results on an I2C LCD.
⚙️ OBJECTIVES
Automate the spice dispensing process
Achieve accurate weight measurement
Interface multiple hardware modules (Servo, LCD, Load Cell)
Implement UART communication between 8051 and Arduino

## Slide 3
PROBLEM STATEMENT
❌
Manual & Inaccurate
Traditional spice measurement is done by hand, leading to imprecise quantities every time.
🍽️
Inconsistent Taste
Inaccurate measurement results in dishes tasting different each time they are prepared.
⏱️
Time-Consuming
Manual dispensing slows down cooking workflows in both home and professional kitchens.
▼ OUR SOLUTION
✅ Automated Dispensing
⚖️ Precise Measurement
🤖 Reduced Human Effort

## Slide 4
SYSTEM OVERVIEW
🔵 8051 MICROCONTROLLER
Handles main program logic
Weight measurement via HX711
I2C LCD display control
Sends UART commands to Arduino
🟡 ARDUINO UNO / NANO
Receives UART signals from 8051
Controls 5 servo motors (Pins 8-12)
Maps signals A-E to dispensers
Rotates servo for dispensing
WORKING FLOW
User Presses Button
→
8051 Detects Input
→
UART Signal Sent
→
Arduino Receives
→
Servo Rotates
→
Weight Measured
→
LCD Displays

## Slide 5
COMPONENTS USED
🔲
8051 MCU
Main controller
⚡
Arduino
Servo driver
🔩
5× Servo Motors
Pins 8–12
⚖️
Load Cell
Force sensor
📡
HX711 Module
24-bit ADC
🖥️
I2C LCD
2-pin display
🔘
Push Buttons
A–E + TARE
🔋
Power Supply
System power
🔌
Wires
Connections

## Slide 6
INTERFACING DETAILS
UART
Arduino Pin 2 → 8051 P3.1
Servo Motors
Arduino Pins 8, 9, 10, 11, 12
I2C LCD
SDA → P2.0 | SCL → P2.1
HX711 Module
DT → P3.2 | SCK → P3.3
Buttons A–E
P1 Pins (button inputs)
TARE Button
P1.1 (calibration trigger)

## Slide 7
WORKING PRINCIPLE
1
System Initialization
LCD and UART are initialized. HX711 module is configured for load sensing.
2
Calibration Phase
User presses TARE. System records empty weight (x0) and known weight (x1) for accuracy.
3
Button Input
User presses any switch A–E. 8051 microcontroller detects the button press.
4
UART Communication
8051 transmits character (A/B/C/D/E). Arduino receives and identifies the signal.
5
Servo Operation
Arduino rotates the corresponding servo motor. Spice is dispensed from the container.
6
Weight & Display
Load cell senses weight → HX711 converts to digital → LCD displays weight in grams.

## Slide 8
CODE EXPLANATION
PHASE 1 — CALIBRATION
User presses TARE → x0 = HX711_Avg_Slow() [empty] → x1 = HX711_Avg_Slow() [known weight]
PHASE 2 — UART COMMUNICATION
if (B0 == 0) UART_Send('A'); if (B1 == 0) UART_Send('B'); if (B2 == 0) UART_Send('C'); ...and so on
PHASE 3 — WEIGHT CALCULATION & DISPLAY
weight = (reading - x0) * CAL_WEIGHT / (x1 - x0);
LCD_String("Weight:"); LCD_Number(weight);

## Slide 9
HX711 LOAD CELL & I2C LCD
⚖️ HX711 + LOAD CELL
▸ Load cell converts applied force into a proportional electrical signal
▸ HX711 amplifies the small analog signal from the load cell
▸ Converts signal to digital via 24-bit ADC for high accuracy
▸ Provides reliable and precise weight readings in grams
▸ DT pin → P3.2 | SCK pin → P3.3 on 8051
🖥️ I2C LCD DISPLAY
▸ Uses only 2 pins: SDA and SCL (saves GPIO)
▸ SDA → P2.0 | SCL → P2.1 on 8051
▸ Displays weight readings in real time (grams)
▸ Shows calibration messages during TARE phase
▸ Efficient, low-wiring I2C communication protocol

## Slide 10
RESULTS & ADVANTAGES
RESULTS
✅ Accurate spice dispensing achieved
✅ Real-time weight display on LCD
✅ Smooth UART communication between controllers
ADVANTAGES
🎯 High precision measurement
🤖 Fully automated system
👆 Easy to use interface
💰 Cost-effective design

## Slide 11
LIMITATIONS & FUTURE SCOPE
⚠️ LIMITATIONS
⚠ Requires manual calibration before use
⚠ Mechanical servo delays can affect timing
⚠ Limited load cell capacity
🚀 FUTURE SCOPE
📱 Mobile app integration
🎙️ Voice control system
🌐 IoT-based monitoring
🤖 AI-based recipe automation

## Slide 12
APPLICATIONS & CONCLUSION
🏠
Smart Kitchens
Automated home cooking
🍽️
Restaurants
Consistent culinary recipes
🏭
Food Processing
Industrial spice packaging
🤖
Automated Cooking
AI-guided meal systems
🎤 CONCLUSION
The Smart Spice Dispenser successfully demonstrates seamless integration of 8051 and Arduino, achieving accurate weight measurement using a load cell with HX711, and automating the dispensing process through servo motors. It provides a reliable, efficient, and smart solution for modern kitchens — reducing human effort while ensuring consistent, precise spice quantities every time.

## Slide 13
THANK YOU
Smart Spice Dispenser Using 8051 & Arduino
Vansh Kukkar · Krish Kumar Kedia · Ronit Vishwakarma · Om Patil · Prashant Kumar Moharana
Department of Electronics & Communication Engineering
24BEC1368 | 24BEC1506 | 24BEC1347 | 24BEC1418 | 24BEC1500